## Slide 1
ERRORS IN CHAINING AND THEIR CORRECTION
Types of error
Mistakes
Systemic or cumulative errors
Accidental or compensating errors
Mistakes / Blunders: - These are due to in experience or to carelessness on
the part of the surveyor or the chairmen. It is random in both occurrence
and magnitude
Examples are: -
Omitting an entire chain length in booking. This is prevented by noting down
each chain length, ad by the leader keeping careful count of the arrows
Mis-reading the chain age by confusing the tallies say the 14m and 16m
tallies on 30m chain. Also the units four and six are capable of being misread.
Only careful reading can prevent these mistakes
Erroneous booking:-Prevented by the chainman carefully calling out the
result and the surveyor repeating it, paying attention when calling 5 or 9 7

## Slide 2: B Systematic or cumulative Errors: - In surveying, systematic errors occur due to natural causes instrumental factors, and the observer’s human limitation, temperature, humidity, and barometric pressure – natural sources that affect angle measurements and distance measurements either by tapes or electronic distance measuring equipment (2) Instrumental factors are caused by either imperfections in construction or lack of adequate adjustment of equipment before their use in data acquisition. e.g. (a) graduations on linear and circular scales, (b) lack of centering of different components of instrument (c) Compromise in optical design, which leaves certain amounts of distortions and aberration (3) Human observer limitations – man relies mostly on the natural senses of vision and hearing, both of which 1/2 limitations and vary due to circumstances and from one individual to another. The set of error committed by an observer depend on the precise physical, psychological, and environmental conditions that exist during the particular observational experiment. There are two such errors in chaining to which corrections are applied. Correction of chain for standardization and correction for sloping ground